## Slide 1: UCS Chassis/Server Discovery
Swapnil Wagh

## Slide 2: Agenda
Chassis Discovery
Blade Server Discovery
  Deep Discovery
  Shallow Discovery
  Service Profile Association
Rack Server Discovery
  Dual Wire Management
  Single Wire Management

## Slide 3: Typical Deployment

## Slide 4: Packet Flow for Internal Vlans
FI (Springfield/Mammoth)
IOM
Redwood/Woodside
CMS
CPU
Server 1
Server N
Adaptor
CIMC
Adaptor
CIMC
. . . . . . .
. . .
. . .
nif
hif
cif
bif
4043/4047
4044
4042

## Slide 5: Internal Networks
IP addressing scheme:
CMC:
127.15.1.<chassis>
127.5/6.<chassis>.254 [vlan 4044]
CIMC:
127.5/6.<chassis>.<slot_no> [vlan 4044]
Adapter:
127.7/8.<chassis>.<device_no>
KVM Ips and Iptables rules
- Apart from this there is 127.3/4.0.<device_id> network which provides connectivity between CMC and CIMC over vlan 1.
- 127.12.0.1 and 127.12.0.2 (Fixed bond0 IPs)
- 127.11.0.1 and 127.11.0.2 (Fixed IP for communication between peer CMC over p2p serial link)

## Slide 6: Chassis Discovery
“Server Port” Configuration by User
  Only internal vlans allowed to prevent any other traffic forwarding
  On IOM, if connected, satctrl will start sending out sdp packets
  Satmgr will receive the sdp packets and identify that an IOM is connected
SAM processes register for MTS_OPC_SAT_DISCOVERED notification
  If_index
  Chassis Serial Number
  Model
  Vendor Details
  *Code and PortAG logs
Numbered list

## Slide 7: Chassis Discovery (contd.)
Depending upon #links connected, #SAT_DISCOVERED messages are sent.
Helps in identifying #links between switch and IOM.
NIF Port vs. Port-channel decision taken based on Chassis Discovery Policy and #min. links required for bring up.
UCSM assigns chassis-id and stores above info along with chassis serial.
  Chassis-id assigned on FCFS basis.
  Chassis id translates to fex-id being configured
  i.e. "switchport mode fex-fabric ; fex associate <chassis-id>”
  Satmgr and Satctrl will exchange the cluster-id, chassis-id.
  Satctrl exchanges this info with CMC using dmclient api.
  Process followed on both IOMs.
CMC on both IOMs will exchange this information to verify their in-sync status.
i.e. Make sure they are being managed by same UCS cluster.
Once this information is verified, SAT_ONLINE happens.
CMC can setup IP addresses dependent on chassis-id.

## Slide 8: Chassis Discovery (contd.)
UCSM[BladeAG] and CMC exchange Chassis inventory information using mctools api.
  mcclient --frus --ip 127.5.<chassis-id>.254
  blade present info from the slot sensor status
Chassis Discovery once all chassis inventory collection is done.
If any blades present, Blade discovery can start now.

## Slide 9: Deep Discovery
Blade presence detected. BMC FRU inventory done.
Verify current h/w config is a valid config to boot the blade.
Blade Power on
Enable HIF ports.
Change boot-order to boot from vmedia. Mount PNUOS as vmedia on the blade host processor.
PNUOS [Processing Node Utility OS] is a small debian linux with all the utilities from the vendors for detailed identification of the h/w components and some UCSM binaries.
Once PNUOS boots, HostAgent on the host handshakes with HostAgentAG on FI.
PNUOS helps in getting detailed inventory. Communicated to UCSM.
Cleanup
  Unmount vmedia
  Reboot blade
  Unconfigure HIFs

## Slide 10: Shallow Discovery
Typically done after a re-acknowledge/reload of the server.
Since the h/w config like adapter, memory, storage etc. is unchanged, no need to initiate a full discovery.
No-shut the HIFs and proceed with service profile association.
Once discovery is complete, SP association can go through
If shallow discovery and a SP was associated before a reboot, UCSM knows which SP is to be associated after the discovery is complete.
For deep discovery, the most common case is fresh installation of the blade. User creates an SP.
SP contains :-
  Boot order
  Creation of vNIC, vHBA
  mac, wwnn, qos, vlan config on them
  etc.

## Slide 11: Rack Server
Challenges:-
  No fixed ports for BMC and Adapter
  Rack-mount servers can be directly connected to the switch or through a FEX
  UCSM High availability is a must for both management and data planes. Rack-mount server connectivity should follow UCS Fabric-A/Fabric-B model
  How to support cisco adapters vs. third-party adapters ?
  How to maintain security, i.e. user might connect a malicious server sending bursts on vlan 4044, that can hog the switch CPU.

## Slide 12: Rack Server Discovery
Discovery Policy
  Automatic
  User-acknowledged
Supported Modes:-
  Dedicated Mode [Default Mode]
  UCSM Managed Mode
    On transition from Dedicated to UCSM Managed, all user configuration lost.
UCSM Managed Mode
  Dual Wire
  Single Wire

## Slide 13: Dual Wire vs. Single Wire
Dual Wire
  Adapter ports and BMC ports separately connected.
  Adapter ports can be connected to switch/fex.
  BMC ports only to fex.
  Use 1G LOM ports for BMC.
  BMC is in “shared LOM” mode
Single Wire
  Same port for BMC and adapter
  Not supported on 3rd party adapters
  All single wire adapters also support dual wire management
  Connectivity through fex and switch(elcap)
  BMC is in “auto” mode

## Slide 14: Port Security
Security required on the ports to prevent unwanted traffic from flowing.
Concept of port-states introduced to allow limited traffic w.r.t. discovery to flow.
Port states maintained by UCSM and not NXOS.
Start state is "unconfigured". Admin shut with no configuration. Default state.
When user configures server port, port state moved to "untrusted". Only sdp, dhcp, lldp traffic on vlan 4044 allowed.
  Control Plane Policer configured with low value to prevent cpu hog.
  Drop everything else.
When discovery is complete, move to "trusted" state. To detect physical connectivity changes, use lldp peer information.
If any change, move to "untrusted" state and trigger a deep discovery.

## Slide 15: Rack Server Discovery – Dual Wire
Configure baseboard ports as server ports. VLAN 4044 allowed on the switch/HIF ports for SAM to communicate with BMC. Port moves from “unconfigured” to “untrusted”
Make 4044 as the native vlan as BMC sends untagged packets.
If fex is present, once HIFs are online, configure FEX HIFs to allow vlan 4044 only natively.
Once the LOM port up is detected, BMC will start sending DHCP requests to the DHCP server running on SAM.
The request includes :-
  Vendor info, serial no.
  BMC mode
  Interface Info (LOM/Adapter)
  Cookie for authentication
Switch on receiving this info, will redirect the packet to muxif. Muxif on validating the DHCP request, inserts option82 in the packet. Option 82 used for if-index. Muxif sends packet to the UCSM.

## Slide 16: Rack Server Discovery – Dual Wire(contd.)
UCSM will also compute a server_id. UCSM replies with a valid lease and cookie. IP assigned from the 127.99 scratchpad n/w. Lease duration very small.
BMC will verify this cookie and move from direct managed to UCSM managed mode.
  start services required for discovery like mcserver etc.
  issue a DHCP request on vlan 4044.
UCSM will reply with an IP based on the server_id as follows :-
"127.5/6.225.0 | server_id ”
UCSM will start communicating with BMC using mctools api for BMC inventory.
  vmedia setup and PNUOS boot will happen next similar to blade server discovery.This will give a complete inventory to UCSM. for e.g. firmware version, memory info etc.
HostAgent sends a dhcp request on the adapter ports. Switch inserts option 82 again to identify adapter port.
Now, (bmc port and adapter port) can be tied to a single rack server.
Ports move to “trusted” state
This completes Rack Server discovery
All ACLs and policer config is removed.

## Slide 17: Rack Server Discover – Single Wire
Once adapter port up is detected, BMC sends DHCP request with [Interface = Sideband(i.e. BMC interface connected to Adapter)] set.
UCSM replies with an IP from 127.99 n/w and a short lease period.
UCSM also sends the port-profile in the dhcp response.
UCSM moves interface to vntag mode.
BMC moves to UCSM Managed mode. BMC moves the nic to niv mode, and provides port-profile received.
Adapter creates mgmt vnic with this port-profile.
BMC sends new dhcp request on vlan 4044, using this mgmt vnic.
Switch replies with IP “127.5.225.0 | server_id”
Rest of the discovery process is the same and completed by mctools.
Service profile association can go through now.

## Slide 18: Backup Slides
Typical Information retrieved by PNUOS
  BIOS: Vendor, Version
  Processor: Socket, Vendor, Model, Speed, Stepping, Arch, Core count, Threads
  Memory: MemSize, Vendor, Model, Serial, Type, Locator, Bank, FormFactor, Set, Speed, Latency, Width
  NIC: SlotId, NicDevice, PCI vendor/device/addr, PortId, MacAddr,EthName
  HBA: SlotId, Id, Vendor, Model, SN, PCIaddr, PortId, wwpn, wwnn, bootwwnn, bootLun, bootLoaderVersion, runningVersion.